## Slide 1: Heuristics for Road Network Augmentation
Bart Jansen, University of Utrecht

## Slide 2: Outline
Problem background
Geometrical problem statement
Research
Experimental evaluation of heuristics
  Heuristics
  Results
Conclusion

## Slide 3: Problem background
Several types of analysis require accessibility information
  Study the relationship between deaths by heart attacks in an area, and the distance to the nearest hospital
Accessibility information also required for various optimization problems
  Facility location problem
What to do if the road network is not fully known?

## Slide 4: Incomplete road networks
Google Maps view of area around Lusaka, Zambia
Map data from developing countries
Known information:
  Locations of settlements
  Major roads
Some settlements are not connected to the road network

## Slide 5: Road network augmentation
Added one feed-link
People “get around”, so some roads must exist
Try to compute roads that seem reasonable, and add them to the network
  Added roads are “feed links”
Metric to compute the quality of feed links

## Slide 6: Geometric problem
Add feed links to connect a village to the road network
Connect point inside polygon to boundary, avoiding obstacles
Find best feed link(s), based on a quality metric

## Slide 7: Metric for network induced detour
Based on the detour you take when traveling over the road network
Network distance between A and B:
  Length of shortest path over the road network
Crow-flight distance between A and B:
  Length of shortest path cross-country that avoids obstacles
Crow-flight conversion factor (CFCF) for AB

## Slide 8: Examples of CFCF
Polygon with feed links
Crow flight conversion factor between p and r
With obstacles
  Feed links avoid obstacles
Multiple feed links
  Use link that yields shortest path

## Slide 9: Metric for network quality
Dilation induced by a set of feed links:
  Maximum CFCF between source point and a point on the boundary
Intuitively:
  Maximum “detour” forced by the road network
Leads to various geometric problems
  Minimize the dilation using exactly k feed links
  Minimize the number of feed links to achieve an dilation of at most d

## Slide 10: Research on feed links
Various theoretical and experimental results
My contribution: experimental evaluation of heuristics

## Slide 11: Experimental analysis
Goal: minimize the dilation using a fixed number of feed links
Hard to solve exactly, for arbitrary numbers of feed links
Three heuristics were experimentally evaluated
Experimentation project for Game and Media Technology
Applied heuristics to 100 randomly generated problem instances, using Java

## Slide 12: Maximum Dilation Heuristic
To place first feed link
  Connect p to closest point on boundary
To place i+1’th feed link
  Connect p to point that has largest CFCF using feed links 1, 2, .. , i

## Slide 13: Sector Heuristic
To place k feed links
  Divide the polygon into k sectors around p
  In each sector, connect a feed link to the closest boundary point
Two strategies for sector orientation
  Greedy
  Random

## Slide 14: Experimental results
Maximum Dilation Heuristic performs best in general
Average dilation of 4.2 for 1 feed link
Observed average approximation ratio of best heuristic close to 1.1
Relative performance of sector heuristics depends on number of feed links
  For 2 feed links, greedy is better
  For 3 feed links, random is better

## Slide 15: Results: average dilation
Chart: Feed links
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Sector [G] | 4.1832 | 2.1765 | 2.2881 | 1.8259 | 1.6803 | 1.6123 | 1.5645 | 1.5379 | 1.4862 | 1.447
Sector [R] | 4.1832 | 2.7468 | 2.1291 | 1.8966 | 1.7292 | 1.6217 | 1.5788 | 1.5306 | 1.4953 | 1.473
Max Dil. | 4.1832 | 2.0862 | 1.8148 | 1.6494 | 1.5527 | 1.4932 | 1.4474 | 1.4187 | 1.3925 | 1.38

## Slide 16: Sector heuristic for 2 feed links
Greedy orientation
Dilation value 2.1
Random orientation
Dilation value 2.6

## Slide 17: Sector heuristic for 2 feed links
Greedy orientation
Dilation value 2.1
Random orientation
Dilation value 2.6

## Slide 18: Conclusion
Road network augmentation has practical use for accessibility analysis using incomplete data
The problem offers interesting scientific challenges
Simple heuristics often perform well

## Slide 19: Sector heuristic for 3 feed links
Greedy orientation
Dilation value 2.4
Random orientation
Dilation value 1.9

## Slide 20: Sector heuristic for 3 feed links
Greedy orientation
Dilation value 2.4
Random orientation
Dilation value 1.9