# Solutions to Exercises for 
Statistics 2 for Chemical Engineering

# Week 4

1. a)  Choose Special -> Experimental Design -> Create Design -> Multilevel Factorial. Do not forget to increase the number of levels for all independent factors (called experimental factors in Statgraphics) to 5.

b) We minimally need 6 terms:

| constant | 1 |
| --- | --- |
| main effects A, B and C | 3 |
| interactions AB and AC | 2 |
| total | 6 |

By right-clicking in the window we may choose the correct options:

By choosing the option Worksheet we directly see which 6 of the 5*5*5=125 possible runs have computed to be a D-optimal design:

By choosing the icon Save Results (to the right of the Graphics icon) we may transfer the design points to the data worksheet. Choosing the menu Plot -> Scatterplots -> XYZ plot we obtain the above picture of the computed design. The above plot has been obtained by improving the plot through conveniently chosen Pane (left) and Graphics (right) options:

We see that the design is asymmetrical: there are 4 points on the bottom of the cube and two in front on top. This reflects the asymmetry of the model (the interaction BC in missing).

2. a) -
b) We minimally need 7 terms:

| constant | 1 |
| --- | --- |
| main effects A, B | 2 |
| interaction AB | 1 |
| quadratic effect A, B | 2 |
| cubic effect A | 1 |
| total | 7 |

c) The runs 1, 14, 27, 97, 175, 189 and 253 were selected.

We see that the design points are on the boundary of the experimental region. There is a slight asymmetry because on the diagonal there is gap near pH = 6.9. This is probably  caused by the fact that there is a cubic term in pH, but not in modifier.

d) The runs 1, 14, 27, 158, 203 and 253 were selected.

We now have a symmetric model and see a more or less symmetric distribution of design points on the boundary of the experimental region.

e) The numbers refer to the design for which D-efficiency is highest. Changes in the choice of the algorithm may heavily influence G-optimality of the selected D-optimal design.

| Number of runs | D-efficiency | A-efficiency | G-efficiency |
| --- | --- | --- | --- |
| 7 | 19.60 % | 5.78 % | 74.01 % |
| 8 | 19.96 % | 6.18 % | 75.68 % |
| 9 | 20.25 % | 5.94 % | 85.68% |
| 10 | 20.23 % | 6.85 % | 87.23 % |
| 11 | 19.96 % | 6.67 % | 85.37 % |
| 12 | 19.87 % | 6.48 % | 80.28 % |
| 13 | 19.85 % | 6.13 % | 78.92 % |
| 14 | 19.89 % | 6.11 % | 85.19 % |

f) and g) Like indicated in the paper, we see that it is not worthwhile to put extra effort in executing more than 9 or 10 experiments. However, the differences are small. Note that there is no scale on the horizontal axis of the graphs in the paper, which makes it hard to draw conclusions. The results on G-efficiency of our designs do not coincide (in particular, for 12 runs).

3. a)

The ANOVA table below indicates that the model is adequate:

The residual plots also indicate that there no violations of model assumptions:

b) There is synergistic interaction between A and B, A and C. There is antagonistic interaction between B and C.

c)

The grey area indicates where yarn elongation is maximal. Because of the difficult shape of this area, it may be sensible to do further experimentation in this restricted region to find optimal settings.

4. a)

There seems to be no lack-of-fit.

b)

This model is not an improvement. First of all, there was no lack-of-fit in the linear model. Secondly, the interaction terms are all not significant. A more formal way of testing would be to compare sums of squares, but this is not covered in this course.

c) For prediction, it is better to use the quadratic model, since it is slightly more precise. For explanation, a linear model suffices.

d)