## Slide 1: On a Generalization of the GCD for Intervals in R+
Stan Baggen
June 4, 2014
or
how can a camera see at least 1 tone for unkown Texp

## Slide 2: Contents
Introduction
Cameras, exposure times and problem definition
Introduction to Solution using GCD for Integer Frequencies
Extension of GCD to intervals over R+
Application to the Original Problem
Discussion
Yet another generalization

## Slide 3: Introduction
Transmit digital information from a luminaire to a smartphone or tablet using Visible Light Communication (VLC)
  Bits are encoded in small intensity variations of the emitted light
  Detect bits using the camera of a smartphone
We consider an FSK-based system
  Symbols correspond to frequencies (tones)
  Emitted light variations are sinusoidal
Problem: camera may be “blind” for certain frequencies

## Slide 4: Camera Image divided into lines and pixels
lines covering source
lines per frame
hidden lines
active lines
Each line consists of a row of pixels

## Slide 5: Exposure Time
A camera can set its exposure time Texp
    typically, Texp ranges from 1/30 to 1/2500 [s]
Each pixel “sees” the average light during Texp seconds before read-out
  smearing of intensity variations of received light
If an integer number of periods of a sinusoid fit into Texp, the camera cannot detect such a sinusoid
time
Texp
ISI filter (moving average)
f1
f2

## Slide 6: Exposure Time
Due to the exposure time Texp of a camera, certain frequencies cannot be detected by it (multiples of fexp = 1/Texp)
Can we have sets of 2 frequencies each, such that not both can be blocked for any fexp ≥ 30 Hz
Each set then forms an fexp-independent detection set for a light source that emits both frequencies
f1
f2
time
Texp
ISI filter

## Slide 7: Discrete Solution
If the involved frequencies can only take on integer values, we can find solutions using the GCD (Greatest Common Divisor) from number theory
We would like to have 2 frequencies f1 and f2, such that not both can be integer multiples of any fexp ≥ 30
Suppose that both f1 and f2 are integer multiples of fexp
If GCD(f1,f2) < 30  no solution possible for fexp ≥ 30  pair (f1,f2) is a good choice

## Slide 8: Discrete Solution: Example
f1 = 290; f2 = 319
Largest integer that divides both f1 and f2 equals GCD(f1,f2) = 29
No integer fexp ≥ 30 exists for which multiples are simultaneously equal to f1 and f2

## Slide 9: Problem with Discrete Solution
GCD(300,301) = 1; GCD(300,300) = 300
Physically: due to the nature of the Texp-filter and detection algorithms, if a pair of frequencies (f1,f2) is bad for detection, then a real interval (f1±ε,f2 ±ε) is also bad
We need a method that allows us to eliminate bad intervals over R+
f1
f2

## Slide 10: GCD for intervals in R+
Consider 2 half-open intervals I1 and I2 in R+
Definition:
Note that the concept I1,I2: GCD(I1,I2) < 30 solves our original problem:
There can be no real fexp≥30 such that integer multiples are simultaneously close to F1 and F2
0
( ]
( ]
I1
I2
0
( ]
( ]
30

## Slide 11: GCD for intervals in R+
How to find GCD(I1,I2)?
Define divisor sets D1,D2 in R:
Theorem 1:
Proof: □
0
( ]
( ]
I1
I2

## Slide 12: Example

## Slide 13
Enlargement of Example

## Slide 14: Overlap of Intervals in Divisor Sets
Consider divisor set
Let where
Theorem 2: for w>0, D consists of a finite number n0 of disjunct intervals, where
Proof: overlap of consecutive intervals happens if
Corollary:
0
( ]
I

## Slide 15: Another Theorem
Suppose that we have 2 intervals I1=(f1-w1,f1] and I2=(f2-w2,f2]
Theorem 3: For w1,w2> 0, GCD(f1,f2 ; w1,w2) equals an integer sub-multiple of either f1, f2 or both
Proof: equals a right limit point of for some i and j. Each is the intersection of 2 half-open intervals (...], where the right limit point of each half-open interval is an integer sub-multiple of either f1 or f2 or both. □
Note: f1 and f2 are real numbers

## Slide 16: Some Interesting Examples
Numbers in N+
  For w sufficiently small, we find the classical solutions for f1, f2 in N+
  GCD(15,21; w≤1) = 3
  GCD(15,21; w=1.1) = 7
    w too large for finding the classical solution
Numbers in Q+
  GCD(0.9,1.2; w=0.1) = 0.3
Numbers in R+ (computed with finite precision)
  GCD(7π,8π; w=0.1) = 3.1416
  GCD(6π,8π; w=0.1) = 6.2832

## Slide 17: Application to the Original Problem
Suppose that we find that for a certain (f1, f2; w1,w2) : GCD (f1, f2; w1,w2) < 30
Then there exists no real number fexp≥30 such that integer multiples of fexp fall simultaneously in (f1-w1, f1] and (f2-w2, f2]
By picking F1= f1-w1/2 and F2= f2-w2/2, we can insure that if one multiple of fexp≥30 falls within a range of wi/2 of Fi for some i, then the other interval is free from any multiple of fexp
0
( ]
( ]
30
f

## Slide 18
Numerical Examples (1)
acceptable_frequencies_2012_10_20_1

## Slide 19
acceptable_frequencies_2012_10_20_1
typical solutions: (f1,f2) = (f1, f1+15)
Numerical Examples (1) detail

## Slide 20
Numerical Examples (2)
acceptable_frequencies_2012_10_18_2

## Slide 21
Numerical Examples (2) detail
acceptable_frequencies_2012_10_18_2

## Slide 22
Numerical Examples (3)
acceptable_frequencies_2012_10_18_3

## Slide 23
Numerical Examples (4)
acceptable_frequencies_2012_10_18_4

## Slide 24
Numerical Examples (4) detail
acceptable_frequencies_2012_10_18_4
typical solutions: (f1,f2) = (f1, f1+15), (f1, 2f1-20), ), (f1, 2f1+15)

## Slide 25: Discussion (1)
It is convenient to use half open intervals (…] and have the right limit point as a characterizing number, since then
  We can reproduce the familiar results from number theory
  The maximum in the definition of GCD exists
  We do not obtain subsets in having measure 0
The concept of GCD can be generalized to an arbitrary number of K intervals over R+
Theorem 2 shows that the complexity of the computation of a GCD is reasonable
Can we have an efficient algorithm like Euclid’s algorithm for computing the GCD of real intervals?

## Slide 26: Discussion (2)
It can be shown that GCD(f1, f2;w) is non-decreasing as w increases
For rational numbers a/b and p/q, where a,b,p,q are in N+, we find for sufficiently small w: where LCM(.) is the Least Common Multiple. How small must w be as a function of a,b,p and q to find this solution?
Conjecture: for incommensurable numbers a and b
Effects of finite precision computations

## Slide 27: Yet Another Generalization
GCD(f1,f2;w) on intervals still makes hard decisions on frequencies being in or out of intervals
Can we make some sensible reasoning that leads to “smooth” decisions concerning acceptable frequency pairs
We have to use a more friendly measure on the intervals
We start by re-phrasing the previous approach in a different manner

## Slide 28
GCD(f1,f2;w) on intervals as discussed previously, effectively uses indicator functions as a measure of membership:
Divisor Measure DM1,DM2 in R+
0
( ]
( ]
I1
I2
1
f

## Slide 29
Example
f1 = 9; f2 = 12
w = 0.5
GCD(f1,f1;w) = 3
9
12
3

## Slide 30: Using a Different Measure
Suppose that we change the definition of the measure of membership for the fundamental interval
Divisor Measure:
Common Divisor Measure:
example

## Slide 31
Example
Multiples of frequencies in the neighborhood of 3 (and 3/n) also end up both near 9 and 12
For frequencies f>3.2, no multiples end up both near 9 and 12 according to the measure
Multiples of 1.1, 1.3 and 1.7 come somewhat close to both 9 and 12 (c.f. other measure)

## Slide 32
Example
If we increase σ, it becomes more difficult to
“avoid” the intervals around 9 and 12 for integer multiples of f
For σ=0.5, some multiples of 4.16 also come close
to both 9 and 12 according to the measure

## Slide 33
f1 = 9; f2 = 12
σ = 0.5
fexp = 4.16
Example
samples taken at integer multiples of 4.16
CDM(4.16;.) equals product of largest “red” sample (n=3) and largest “blue” sample (n=2)