## Slide 1: Real-time analysis
2IN60: Real-time Architectures (for automotive systems)

## Slide 2: Goals for this slide set
Describe the real-time scheduling model with all the relevant parameters
Explain the difference between necessary, sufficient and exact schedulability conditions
Explain the notion of a critical instant
Describe the utilization and worst-case response time analysis (including all relevant equations)
Apply the utilization and worst-case response time analysis to a real-time system
Describe how context switches and interrupt handling can be incorporated in the analysis

## Slide 3: Outline
Real-time scheduling model
Worst-case schedulability analysis
  Schedulability conditions
  Critical instance
  Utilization analysis
  Response time analysis
Practical factors
  Activation jitter
  Context switches
  External interrupts
  Timer interrupt

## Slide 4: Modeling software systems
When investigating the root causes for traffic jams in a city, it is infeasible to consider the interactions between molecules comprising the car or the driver’s brain
A model is an abstraction of the key elements which are relevant for achieving a given goal
  Example: traffic in a city can be modeled by means of a queue network representing the streets, and Markov chains describing the arrival of cars
Notes: It is crucial to stress that every model serves a particular purpose.

## Slide 5: A basic scheduling model
Model (of a system in general):
  Abstraction (of that system)
    leaving out details irrelevant to a given set of criteria
    preserving the properties of interest
Scheduling model (for Real-Time Software)
  explicitly addresses relevant issues in real-time systems
  ...but must be mapped eventually onto an execution environment
    OS, hardware, run-time system, ...

## Slide 6: A basic scheduling model
Event:
  Indicates a state change requiring a timely response, i.e. neither too early nor too late
  Internal (e.g. one task triggering another task)
  External (e.g. interrupt from a sensor)
  Timed (e.g. activation of a periodic task)
Task: actions in response of event
  Task instance is termed a job
  A periodic task will generate infinitely many jobs with given period and offset
Processor: executes a single task at a time
Schedule: assignment of tasks to processor during runtime
Notes: RTS: Real-Time System

## Slide 7: Task attributes
A task i has
  name (the ith task) i
  computation (or execution) time Ci
  relative deadline Di
  period (sometimes) Ti , Tmini ,Tmaxi
  phasing (activation of job 0) φi
A job i,k has
  activation (or release) time ai,k
  absolute deadline di,k
  start (or begin) time si,k
  finalization (or end) time fi,k
time
Ci
Ti
ai,k+1
ai,k
si,k
job i,k
fi,k
di,k
+
Notes: “relative” deadline: relative to the activation of the task.
Question: is this model complete?
Answer: NO!
Incomplete:
only worst-case computation time (WC), no best-case (BC);
only a worst-case deadline (D), no best-case deadline (BD);
only minimum inter-arrival time (WT), no maximum (BT);
no activation jitter (AJ);
Hence, the lower-bound on (system) response times can not be taken into account using this model!

## Slide 8: Task deadlines
Deadline: the latest time before which a job must complete
  Relative: Di (relative to the job activation time ai,k)
  Absolute: di,k = ai,k + Di
The consequences of a job missing its deadline (i.e. providing a response after the deadline) determine the type of deadline
di,k
ai,k
Di
time
release
deadline

## Slide 9: Deadline types
Soft
  A response is still valuable after the deadline, but value decreases steadily after that
    Example: interaction with human users. People get impatient.
Firm
  A response has no value after the deadline
    Example: a video frame that cannot be shown in time can be skipped
Hard
  Damage is done if a response does not come in time.
    Example: signal to inflate the airbag
Notes: Firm:
going to the door after the person has left doesn’t make sense.
a car that drove through red, but is no longer “visible” can’t be recorded.
Hard: damage can be hazardous (cars, power-plants) but also economical (brand, turn-over)

## Slide 10: Derived attributes
ai,k = i + kTi activation time of job i,k of a periodic task i
Ui = Ci / Ti utilization of task i
U = ∑ Ui total utilization of task set
Ri,k = fi,k – ai,k response time of job i,k
k
Notes: response time: basis for a schedulability test, i.e. Ri,k≤ Di
hyper-period: when tasks arrive strictly periodically, the pattern of task-arrivals repeats after the hyperperiod.
lateness: positive when too late (finalization time afterdeadline).

## Slide 11: Schedule
Definition:
  Set of n tasks  = {1, …, n}
  Schedule is a function mapping the processor at any time to one task from the task set
    : R → ∪{⊥}, where (t) = ⊥ means idle
Fixed priority preemptive scheduling (FPPS)
  De-facto standard in the industry
    From simple control applications …
    to large defense and aero-space applications
  Supported by commercial RTOS (e.g. μC/OS-II)
  Definition:
    Each task is assigned a unique fixed priority
    At any time the processor is assigned to the highest priority ready task

## Slide 12: Schedule: example
FPPS schedule  of three independent tasks 1, 2, 3, where 1 has highest the priority and 3 the lowest priority
3
2
1
⊥

## Slide 13: Outline
Real-time scheduling model
Worst-case schedulability analysis
  Schedulability conditions
  Critical instance
  Utilization analysis
  Response time analysis
Practical factors
  Activation jitter
  Context switches
  External interrupts
  Timer interrupt

## Slide 14: Schedulability conditions
Requirement:
  all jobs of all tasks of  must meet their deadline constraints, i.e.
Derived notions for task i
  Worst-case response time WRi
  Critical instant: a (hypothetical) instant that leads to WRi
Notes: Given an interval [a, b) with a < b,
the maximum does not exist and the supremum is equal to b;
the minimum and the infimum are both equal to a.
Given an interval (a, b] with a < b,
the maximum and the supremum are both equal to b;
the minimum does not exist and the infimum is equal to a.
Note that BRi≤ WRi by definition.

## Slide 15: Schedulability conditions
Types of conditions:
  Necessary condition
  Sufficient condition
  Exact condition
Examples:
  Necessary condition: Ci  Di
  Sufficient condition: utilization analysis (see later)
  Exact condition: worst-case response time analysis (see later)
Notes: Question: What if sufficient condition doesn’t hold?
Answer: You don’t know if the set will be schedulable, i.e. the task set might be schedulable.
Question What do you know if necessary condition holds?
Answer: You don’t know if the set will be schedulable, i.e. the task set might be schedulable.

## Slide 16: Terminology
Preemption
  Interference from higher priority tasks and ISRs
Blocking
  Interference from lower priority tasks
Interruption
  Arrival of an interrupt and consequently its ISR
  Leads to a preemption of a task (since ISRs have higher priority than tasks)

## Slide 17: Overview of basic assumptions
Events: implicit
Set  of n tasks 1, …, n:
  Released periodically
  Arbitrary phasing
  No self-suspension
  A job does not start before previous job completed (fi,k-1  si,k)
  Hard deadlines and Di  Ti
Single processor
Scheduling:
  FPPS with unique priorities
  Instantaneous pre-emption and non-idling
  Overhead of context switching and task scheduling is ignored
Notational convenience:
  Tasks are given in order of decreasing priority
    i.e. 1 has highest priority and n has lowest priority
Notes: Implicit events: we don’t care whether the tasks are triggered by external events (event-triggered) or timers (time-triggered)

## Slide 18: Utilization analysis (independent tasks)
Assumptions (additional):
  Rate monotonic priority assignment
    Smaller period means higher priority
  Deadlines equal to periods: i.e. Di = Ti
  Independent tasks
    i.e. no resource sharing and no precedence constraints
Necessary condition: U  1
Sufficient condition: U  n (21/n – 1), where n = ||
  RHS is strictly decreasing in n
  Converges to ln(2) (≈ 0.69) for n  
  LL(n) = n (21/n – 1), called the Liu and Layland bound for n tasks
  See [Liu and Layland 73]
Notes: Hence, periodic tasks only.

## Slide 19: Utilization analysis
0
1
n(21/n-1)
?
Utilization
schedulable
not schedulable

## Slide 20: Utilization analysis: example
Task set  consisting of 3 tasks:
Notes:
  RM priority assignment and Di = Ti (RMS)
  Necessary condition:
    U1 + U2 + U3 = 0.97  1, hence  could be schedulable
  Sufficient condition:
    U1 + U2 + U3 = 0.97 > LL(3)  0.78, hence  could be not schedulable
  Hence, another test required
Task | T | C | U
1 | 10 | 3 | 0.30
2 | 19 | 11 | 0.58
3 | 56 | 5 | 0.09

## Slide 21: Utilization analysis (dependent tasks)
Assumptions (additional):
  Rate monotonic priority assignment
  Deadlines equal to periods: i.e. Di = Ti
  Dependent tasks: tasks may share mutually-exclusive resources
Necessary condition:
Sufficient condition:
where n = ||
See [Sha et al 90]

## Slide 22: Critical Instant
Critical instant for task i: scenario when I assumes its WRi.
time
0
10
20
1
2
C2 + C1
C2 + 2C1
1
2
Task 2 is preempted by a single
activation of the higher priority task 1.
The interference increases when the
activation of task 1 is advanced.

## Slide 23: Critical instant: independent tasks
A critical instant occurs upon a simultaneous release of a task with all its higher priority tasks
  Note: “A” rather than “the”, because there may be more instants for which i “assumes” its WRi

## Slide 24: Critical instant: dependent tasks
Blocking time Bi:
  Longest time i can be blocked by lower priority tasks
  Depends on the resource access protocol
    Disabling interrupts or scheduler:
      longest critical section of a lower priority task
    Mutex with Priority Calling Protocol:
      (complicated, see literature)
    Mutex with SRP:
      longest critical section of a lower priority task with a resource ceiling higher or equal to the priority of i

## Slide 25: Critical instant: dependent tasks
A critical instant occurs upon a simultaneous release of a task with all its higher priority tasks, and all lower priority tasks contributing to the worst-case blocking time have executed an ϵ time of their critical section

## Slide 26: Worst-case response time analysis (independent tasks)
Additional assumptions:
  Independent tasks
    i.e. no resource sharing and no precedence constraints
Worst-case response time of a task:
  Longest possible response time among all task jobs:
  WRi = supk (fi,k – ai,k)
Methods for analysing a critical instance:
  Timeline
  Calculation

## Slide 27: WCRT methods: timeline
time
0
10
20
30
40
50
60
1
3
2
WR3 = 56
WR2 = 17
WR1 = 3
 | T | C
1 | 10 | 3
2 | 19 | 11
3 | 56 | 5

## Slide 28: WCRT methods: calculation
  Recursive equation for task i:
  WRi is the smallest positive solution for x
  Assume a task j with a higher priority than i;
    x/Tj denotes the maximum number of preemptions of task i in an interval [0, x) by task j;
    x/TjCj denotes the maximal preemption time of task i in an interval [0, x) by task j.
  Intuition:
    LHS: amount of time available (or provided) in [0, x);
    RHS: max. amount of time requested in [0, x) by i and j < i : j.

## Slide 29: WCRT methods: calculation
Iterative procedure:
  Stop when either:
    WRi(k+1) = WRi(k) (which is the value of WRi)
    the deadline Di is exceeded (hence, not schedulable).
  All intermediate values are at most equal to WRi;
  The procedure terminates when  j < i: Uj < 1.
  See [Harter 84], [Joseph et al 86] or [Audsley et al 91].

## Slide 30: WCRT methods: calculation
Example for task 3:
  WR3(0) = C3 + j < 3: Cj = 5 + 3 + 11 = 19
  WR3(1) = C3 + j < 3: WR3 (0)/TjCj = 5 + 19/103 + 19/1911 = 5 + 23 + 111 = 22
  WR3(2) = 5 + 22/103 + 22/1911 = 5 + 33 + 211 = 36
  WR3(3) = 5 + 36/103 + 36/1911 = 5 + 43 + 211 = 39
  WR3(4) = 5 + 39/103 + 39/1911 = 5 + 43 + 311 = 50
  WR3(5) = 5 + 50/103 + 50/1911 = 5 + 53 + 311 = 53
  WR3(6) = 5 + 53/103 + 53/1911 = 5 + 63 + 311 = 56
  WR3(7) = 5 + 56/103 + 56/1911 = 5 + 63 + 311 = 56
  Because WR3 (6) = WR3 (7) = 56 ≤ D3 = T3, WR3= 56.
 | T | C
1 | 10 | 3
2 | 19 | 11
3 | 56 | 5
Notes: Write the example (slide 5) on the board, and ask the students to derive WR_3 using the formulas on the previous slide (11).

## Slide 31: WCRT methods: calculation
WR3(2) = 5 + 33 + 211 = 36
WR3(0) = 5 + 3 + 11 = 19
WR3(1) = 5 + 23 + 111 = 22
56
19
22
36
53
39
50
WR3(6) = WR3(7) = 5 + 6·3 + 3·11 = 56
time
0
10
20
30
40
50
60
1
3
2
6
5
4
3
2
1
2
1
3
 | T | C
1 | 10 | 3
2 | 19 | 11
3 | 56 | 5

## Slide 32: Worst-case response time analysis (dependent tasks)
Additional assumptions
  Dependent tasks: tasks may share mutually-exclusive resources
Worst-case response time analysis:
  Recursive equation for task i:
  WRi is the smallest positive solution for x
Notes: Note: While it is assumed to be, in the literature it was never proven that worst-case response time analysis for dependent tasks is exact (only for independent tasks).

## Slide 33: Be aware!
The presented analysis has the explicitly stated assumptions as preconditions!

## Slide 34: Outline
Real-time scheduling model
Worst-case schedulability analysis
  Schedulability conditions
  Critical instance
  Utilization analysis
  Response time analysis
Practical factors
  Activation jitter
  Context switches
  External interrupts
  Timer interrupt

## Slide 35: From external event to task activation
Steps:
  External event occurs;
  Detection by sensor;
  Interrupt generated by sensor
    may take some time before the bus is free
  Interrupt arrival at CPU
    may take some time before the interrupt is handled
  Immediate interrupt service
    may be pre-empted by higher priority interrupts
  Activation of the scheduler
    may be delayed to the next clock-tick
  Activation of the task
hence, both a delay and potential jitter between the arrival of the external event and activation of the task!
Notes: ...and similar from activation command by task to real response, also giving rise to delay and jitter of the output...

## Slide 36: Activation jitter

## Slide 37: Activation jitter
Extension of the recursive equation
  AJj is the activation jitter of task j

## Slide 38: Context switches
Question: how many jobs of another task can a job pre-empt, assuming independent tasks?
Answer: at most 1!
Let CS denote the context-switch time of the system, i.e.
  max time the system spends on a context switch;
  optionally including time of the scheduler to service the event interrupt that triggered the context switch
i
j
context switch
Notes: Answer: at most 1
But… what about dependent tasks, with mutexes implemented by Priority Calling Protocol?
Suppose
a lower priority (LP) task locks a resource R;
is subsequently preempted by a higher priority (HP) task;
that is subsequently blocked on R, allowing the LP task to continue;
till the LP task unlocks the resource R, enabling the HP task again.
Note that is can only happen when the LP has already locked the resource R.
Hence, it depends on the time needed for locking on the one hand and context switching on the other.
Moreover, it depends on the number of HP tasks that may block on the task.
Similarly, we may have to take blocking due to LP tasks into account as well...
Question: How about SRP?
Answer: No problem, because tasks are never blocked (only delayed).
See also CSR-08-26 by Mike, Section 5.

## Slide 39: Context switches
Extending the analysis:
  Replace Cj by Cj + 2CS;
  Replace Ci by Ci + 2CS;
Questions:
  Can these extensions be applied for the necessary condition, sufficient condition, and response-time analysis?
  Can you ignore the context switch out-of a task in the response time analysis of that task, i.e. use Ci + CS rather than Ci + 2CS?
Notes: Answer:
• Yes, because you basically “inflate” the computation time with the context-switching time.
• Yes, assuming the response has been “provided” before the last context switch (out of the task after its completion)

## Slide 40: External interrupts
Interrupt service routines will pre-empt a running task ;
  even when the sporadic task handling the interrupt has a lower priority than .
Let
  Tk: the minimum inter-arrival time of the interrupt triggering interrupt service routine k;
  x: the set of external interrupts;
  Ck: the cost of handling that interrupt.
Extension of the recursive equation

## Slide 41: Clock interrupt
Similar to external interrupts
Extension of the recursive equation
Notes: Optional refinement:
  distinguish between
    a fixed cost to serve the clock interrupt;
    additional costs to “move” tasks from the waiting queue to the ready queue
Question: How to model the additional costs?
Answer: an artificial task per lower priority task with:
- a period equal to that lower priority task and
- a computation time corresponding with the cost of the move.
Note: higher priority tasks have been taken into account by means of the context-switch cost.
Additional note: that artificial task runs at highest priority (i.e. the same priority as the clock)…

## Slide 42: Summary of mutual exclusion primitives
Primitive | Pros | Cons
Disable interrupts | Avoid deadlock Simple implementation Simple analysis Prevent interference from interrupts | Higher priority tasks not sharing resources are penalized Interrupts can be missed
Disable scheduler | Avoid deadlock Simple implementation Simple analysis Allow interrupts | Higher priority tasks not sharing resources are penalized Cannot guard resources shared with ISRs
Mutex | Allow interrupts Higher priority tasks not sharing resources are not penalized Avoid “unbounded” priority inversion | Can lead to deadlock (depends on implementation) Cannot guard resources shared with ISRs Suspension not allowed in ISRs
Semaphore | Allow interrupts Higher priority tasks not sharing resources are not penalized | Can lead to deadlock Cannot guard resources shared with ISRs Suspension not allowed in ISRs “Unbounded” priority inversion

## Slide 43: References
Recommended reading:
  [Burns] Ch. 11.2–6, 11.8
Optional reading:
  [Audsley et al 91] N.C. Audsley and A. Burns and M.F. Richardson and A.J. Wellings, Hard Real-Time Scheduling: The Deadline Monotonic Approach, In: Proc. 8th IEEE Workshop on Real-Time Operating Systems and Software (RTOSS), pp. 133-137, May 1991.
  [Harter 84] P. Harter, Response times in level-structured systems, Department of Computer Science, University of Colorado, USA, Tech. Rep. CU-CS-269-84, 1984.
  [Joseph et al 86] M. Joseph and P. Pandya, Finding Response Times in a Real-Time System, The Computer Journal, 29(5): 390-395, 1986.
  [Liu and Layland 73] C.L. Liu and J.W. Layland, Scheduling Algorithms for Multiprogramming in a Real-Time Environment, Journal of the ACM, 20(1): 46-61, January 1973.
  [Sha et al 90] L. Sha, R. Rajkumar, J.P. Lehoczky, Priority inheritance protocols: An approach to real-time synchronization, IEEE Transactions on Computers, 39(9), September 1990
Notes: [Audsley et al 91] N.C. Audsley and A. Burns and M.F. Richardson and A.J. Wellings, Hard Real-Time Scheduling: The Deadline Monotonic Approach, In: Proc. 8th IEEE Workshop on Real-Time Operating Systems and Software (RTOSS), pp. 133-137, May 1991.
[Harter 84] P. Harter, Response times in level-structured systems, Department of Computer Science, University of Colorado, USA, Tech. Rep. CU-CS-269-84, 1984.
[Joseph et al 86] M. Joseph and P. Pandya, Finding Response Times in a Real-Time System, The Computer Journal, 29(5): 390-395, 1986.
[Liu and Layland 73] C.L. Liu and J.W. Layland, Scheduling Algorithms for Multiprogramming in a Real-Time Environment, Journal of the ACM, 20(1): 46-61, January 1973.
[Sha et al 90] L. Sha, R. Rajkumar, J.P. Lehoczky, Priority inheritance protocols” An approach to real-time synchronization, IEEE Transactions on Computers, 39(9), September 1990