## Slide 1: Communication
2IN60: Real-time Architectures (for automotive systems)
(many slides are by courtesy of Damir Isovic)

## Slide 2: Goals for this slide set
Describe the CAN protocol
Explain how to use the CAN driver API under μC/OS-II
Apply the response-time analysis to a real-time system comprised of nodes communicating via a CAN bus

## Slide 3: Outline
Introduction to communication in automotive real-time systems
CAN protocol
Timing properties
Schedulability analysis
CAN under μC/OS-II

## Slide 4: Summary of real-time primitives so far
Cyclic executive (AFAP, periodic)
  Goal: several tasks executing on the same ECU
Preemptive scheduler
  Goal: higher priority Task1 preempts a long Task2
Disabling/enabling interrupts/scheduler
  Goal: execute a portion of a task non-preemptively
Mutex
  Goal: Task1 and Task2 share a resource (shorter blocking time than disabling interrupts or scheduler)
Semaphore
  Goal: Task1 triggers Task2 running on the same ECU
Communication
  Goal: Task1 triggers Task2 running on a different ECU

## Slide 5: Example: distributed control
Task1:
Triggered periodically
Senses the light and sends
the reading to another ECU
Task2:
Triggered by arriving light reading
If the reading exceeds threshold,
turns on a LED

## Slide 6: Example: distributed control
Requires communicating the sensed value with another ECU
Communication requires a protocol
  Protocol describes the frame (message) format, frame sequence, timing, physical constraints, …
  Infeasible to have a different protocol for every sensor/ECU
  Standard protocols used in automotive: CAN, FlexRay

## Slide 7: RT communication used to look like this…
It used to look like this…
As the number of electronic devices grew
  the wiring gets more “messy”
  the weight of the car increases
Notes: In 2002 over 4km of wiring in a car

## Slide 8: Network architecture of a car
In modern cars, point-to-point wiring is replaced by a common communication bus
Bus
  Connects individual ECUs
  Examples: CAN, FlexRay
Interconnect between buses
Benefits:
  Cost reduction
  Flexibility

## Slide 9: Polling based sensing
Check for a condition at regular intervals
  Busy-waiting: check continuously
    E.g. implementation of the ATD driver: check continuously if the status flag in the ATDSTAT register was written (indicating ATD conversion was completed)
  Suspension: check again after a delay
    E.g. alternative implementation of the ATD driver: delay (and suspend) between consecutive checks of the ATDSTAT status flag

## Slide 10: Polling based sensing
Shortcomings:
  Wasted processor cycles (which could be otherwise used to do more useful work, or save energy)
    Note: some devices may provide only means for polling
  Polling period sets a lower bound on event handling latency
    Potentially long latency between the occurrence of an event and its handling

## Slide 11: Interrupt based sensing
Interrupts are hardware signals generated by external hardware indicating that handling is needed
  Arriving interrupt releases a corresponding ISR
  May result in the triggering of a task
Examples:
  Timer has expired
  CAN message has arrived
Notes: External vs. Timer interrupts: external occur at unpredictable moments, while timed interrupts we can predict and even manage (n.b. this is the main thing we can control about a timer interrupt).

## Slide 12: Polling vs. interrupts
Polling:
  Task (periodically) checks for a condition
  Predictable time when the condition is checked
  Time-triggered: due to the timer interrupt
    i.e. timer interrupts can be used to implement polling
Interrupts:
  Task is notified when a condition is satisfied
  Unpredictable time when the condition is satisfied
  Event-triggered: due to any other interrupt

## Slide 13: Time-trigged communication
Node 1
Node 2
Task A
Task B
Task C
Task D
Task E
NW
response
polling

## Slide 14: Event-trigged communication
Node 1
Node 2
Task A
Task B
Task C
Task D
Task E
NW
interrupt
response

## Slide 15: Protocols suitable for real-time communication
TDMA
Time-trigged (periodic)
High testability
Example: TTP-protocol
Node 1
Node 2
Node 3
Node 4
Node 1
Max waiting time = 1 TDMA round
Node 1
Node 2
Node 3
Node 4
Collision
resolution
Highest prio sends
CSMA/CR
Priority based (online schedule)
Flexible
Example: CAN-protocol
Notes: TDMA: Time Division Multiple Access
Static division of channel capacity into a number of slots, and a unique slot is assigned to every node.
TTP (Time Triggered Protocol): designed by Kopetz 1993.
CSMA – Carrier Sense Multiple Access
CD: Collision Detection (e.g Ethernet, not suitable for real-time communication because of unpredictable back-off period)
CA: Collision Avoidance (e.g. WiFi, wait for idle time before transmitting to avoid collisions)
CR: Collision Resolution

## Slide 16: Outline
Introduction to communication in automotive real-time systems
CAN protocol
Timing properties
Schedulability analysis
CAN under μC/OS-II

## Slide 17: CAN – Control Area Network
Originally developed for automotive industry needs
  1983: BOSCH starts CAN development (Intel joins 1985)
  1987: First CAN chip
  1990: First car with CAN (Mercedes S-class)
  1993: ISO standard
Now used also in factory automation
  Very common in machinery
  CAN-controllers developed by Philips, Intel, NEC, Siemens …
An implementation of CSMA/CR
  CSMA/CR: Carrier Sense Multiple Access / Collision Resolution
  Priority based
  CR is the central mechanism
  Bitwise arbitration to resolve collisions

## Slide 18: Structure and function
Synchronous serial communication
A shared medium (cable) with connected nodes
Each frame (or message) is comprised of a sequence of bits
Broadcast: transmitted frames can be picked up by all attached nodes
1 Mbit/s at 40m bus length
Behaves as an AND-grind: bus value = AND between all bits on the bus
Node A
Node B
Node C
Node D
< 40m 1Mbit/s

## Slide 19: Frame types
Data frame
  Carries data from a transmitter to the receivers
Error frame
  Transmitted by any node on detecting a bus error
Remote frame
  Transmitted by a node to request the transmission of the data frame with the same identifier
Overload frame
  Used to provide an extra delay between the preceding and succeeding data or remote frames, e.g. when the buffer of a receiver is full
Notes: We will focus only on the data and error frames.

## Slide 20: CAN data frame
SOF | ID | RTR | Control | Data | CRC | CRC DEL | ACK | ACK DEL | EOF | IFS
1 bit | 11 bits | 1 bit | 6 bits | 0-8 bytes | 15 bits | 1 bit | 1 bit | 1 bit | 7 bits | min 3 bits
SOF - Start of Frame, start bit (always 0), used for signaling that a frame will be sent (the bus must be free)
ID - Identifier, identity for the frame and its priority
RTR - Remote Transmission Request
Control - indicates the length of the data field
Data - message data
CRC - Cyclic Redundancy Check,
CRC DEL - CRC delimiter (always 1)
ACK - Acknowledgement
ACK DEL - ACK delimiter (always 1)
EOF - End of Frame (always 1)
IFS - Inter Frame Space, resending wait time (always 1)
Notes: The identifier serves twopurposesbeyondsimplyidentifying the message:
the identifier is used as a priority todeterminewhichmessage,amongstthosecontendingfor the bus, willbetransmitted next;
the identifiermaybeusedby receivers to filter out messagesthey arenotinterested in, andsoreduce the load on the receiver’s host microprocessor.

## Slide 21: Arbitration mechanism
A node wants to send a frame
Bus
free?
Put ID-bit 0 on the bus
Read bus value
Same as the
one we put?
Yes
No
No
Put the next bit
Yes
Read bus value
Same as
the one we
put?
Last bit?
Send the rest of the frame
Yes
No
Yes
No
CAN bus performs a logical AND on
all bits which are currently put on the bus.
Notes: Reminder: we assume that the bus value = AND between all bits on the bus! (i.e. 0 is ‘dominant’ and 1 is ‘recessive’)

## Slide 22: Arbitration mechanism
Example:
Assume a simplified CAN-system with only three ID-bits and three nodes A, B, C:
A ID=010
B ID=100
C ID=011
000 – highest priority
111 – lowest priority
which gives:
A-high prio, C-middle, B-low
How does the arbitration look like if the nodes are sending simultaneously?
Bit 0
Bit 1
Bit 2
0
1
0
1
1
0
1
Send the rest of the frame
abort! (bit 0  bus value)
abort! (bit 2  bus value)
Node
ID
A
B
C
010
100
011
Bus value:
0
1
0

## Slide 23: CAN error frame
Error detection using the Cyclic Redundancy Check (CRC)
  The CRC is used by receiving nodes to check for errors in the transmitted frame
  If the frame is received correctly, the ACK-bit (in the transmitted data or remote frame) is set to 0
Error signaling
  The node that detects an error puts instantly an error flag (000000 or 111111) on the bus, followed by an error frame
EF | SEF | ED | IS
6 bits | 0..6 bits | 8 bits | 3 bits
EF - Error Flag
SEF - Superposed Error Flag
ED - Error Delimiter
IS - Interframe Space

## Slide 24: Bit stuffing
We must avoid two bit-patterns that are used for error signaling (i.e. 000000 and 111111)
  Bit stuffing: sender puts extra bits on strategic places to prevent forbidden bit-patterns:
    After a sequence of 5 same bits, insert an opposite bit
  Receiver reconstructs the original frame by removing the extra bits
Example:
…00101000000101…
Original frame:
Sender puts extra bits:
…001010000010101…
Receiver removes extra bits:
…00101000000101…
Bits sent on the bus:
…001010000010101…
Notes: Note that bits are transmitted from left to right.
Note that the extra one is added always, irrespective of what is following the 5 zeros, i.e. 00000 1 -> 00000 11.

## Slide 25: Outline
Introduction to communication in automotive real-time systems
CAN protocol
Timing properties
Schedulability analysis
CAN under μC/OS-II

## Slide 26: Traffic model
Abstraction of CAN network:
  Frames in priority queues
  No pre-emption
B
D
A
C
A
B
C
D
Resp time
Removed after sending
A buffer storing frames ready for sending
Sending frame i takes
Ci time
Notes: During this presentation we will assume infinite queues.

## Slide 27: Timing properties
CAN is time deterministic
  The latency can be predicted
  Possible to calculate how long it takes to deliver a frame
SOF | ID | RTR | Control | Data | CRC | CRC DEL | ACK | ACK DEL | EOF | IFS
1 bit | 11 bits | 1 bit | 6 bits | 0-8 bytes | 15 bits | 1 bit | 1 bit | 1 bit | 7 bits | min 3 bits
Sum = 47 + 8n (n = nr of data bytes)
How many bits are sent in a CAN-frame?

## Slide 28: Timing properties
Now we can calculate the total transmission time for a CAN-frame:
Transmission times for 1Mbit/s (i.e. tbit = 1μs):
  longest: nmax= 8:
  shortest: nmin= 0:

## Slide 29: Timing properties (with bit stuffing)
Do we need to perform bit stuffing on all 47+8n bits?
SOF | ID | RTR | Control | Data | CRC | CRC DEL | ACK | ACK DEL | EOF | IFS
1 bit | 11 bits | 1 bit | 6 bits | 0-8 bytes | 15 bits | 1 bit | 1 bit | 1 bit | 7 bits | min 3 bits
34+8n affected bits
In worst-case, 1 extra bit after 5 same bits gives:
Nr of extra bits =
  No. By forbidding some ID values we can avoid bit stuffing in the frame ID. So, only 34 (of 47) control bits are affected.

## Slide 30: Timing properties (with bit stuffing)
Is this correct?
  Not completely. We might need to stuff even more extra bits:
  The standard allows both 000000 and 111111 for error signaling.
  The opposite bit is inserted after every sequence of same 5 bits
Original:
1111 1000 0111 1000 0111 1
After bitstuffing:
To avoid forbidden bit patterns we may need to insert 1 extra bit after the first 5 bits and 1 extra bit after each 4 original bits.
1111 10000 01111 10000 01111 1
Extra bit after 5 original bits
Extra bit after 4 original bits
Extra bit after 4 original bits
Extra bit after 4 original bits
..etc…
  Example:
Notes: Question: Why would you guard against both the 000000 and 111111 when only one of them is implemented? Answer: The CAN controller does not care if it is 0 or 1, which is the dominant piece - it puts in an extra (inverted bit) when it detects 5 same pieces. In this way, the same controller can be used in both the 1- and 0-based systems

## Slide 31: Timing properties (bit stuffing)
Hence, the number of extra bits in a CAN-frame is:
Now we can calculate the total transmission time for a CAN-frame:
Transmission times for 1Mbit/s (i.e. tbit = 1s):
longest: nmax= 8 and including stuff-bits
shortest: nmin= 0 and without extra bits:

## Slide 32: Outline
Introduction to communication in automotive real-time systems
CAN protocol
Timing properties
Schedulability analysis
CAN under μC/OS-II

## Slide 33: Response time analysis for CAN
CAN is priority based. Can we use some kind of response time analysis (similar as for tasks)?
  Yes, with a slight modification. The CAN-bus is non-preemptive, so when a frame has managed to send the first bit, then it will continue sending the rest of the frame (without fear of being preempted by high priority frames)

## Slide 34: Response time analysis for CAN
Response time for frame with priority/id i (pessimistic):
where the blocking time for a frame is given by:
  hp(i) = high priority frames (that can delay the first bit)
  lp(i) = low priority frames (that can block the first bit)

## Slide 35: Outline
Introduction to communication in automotive real-time systems
CAN protocol
Timing properties
Schedulability analysis
CAN under μC/OS-II

## Slide 36: Example: CAN under μC/OS-II
Task1:
Triggered periodically
Senses the light and sends
the reading to another ECU
Task2:
Triggered by arriving light reading
If the reading exceeds threshold,
turns on a LED

## Slide 37: CAN under μC/OS-II
Notes: Messages, when received, are stored in the internal message buffer. When a message with id Xis received, a pointer to the location in the buffer in which it is stored is placed in all the queues which were registered (during the CAN setup) to receive messages with id X. Using the µCOS/II API (i.e. OSQPend() function), we can block until such a pointer arrives in our queue.
Note that the retrieved message pointer points to a buffer owned by the driver. The driver must therefore be informed when a message is not used anymore, so that the message buffer can be reused.

## Slide 38: CAN under μC/OS-II (initialization)
CAN_RESULT CANInit(void)
  Initializes the data structures used internally by the CAN driver. Must be called before calling any other CAN function.
  Returns:
    CAN_OK
    CAN_NO_SEMAPHORE
CAN_RESULT CANConfigureBaudrate(INT32U baudrate, INT8U syncjump)
  Takes a baudrate (in bits per second) and a value for the CAN synchronisation jump (use a value of 0 for default).
  Returns:
    CAN_OK
    CAN_USER_ERROR if the function could not find a way of achieving the desired baud rate.

## Slide 39: CAN under μC/OS-II (initialization)
CAN_RESULT CANStart(void)
  Starts the CAN driver. After this call, the messages arriving on the CAN interface will be written to the appropriate queues (registered earlier).
  Returns: CAN_OK

## Slide 40: CAN under μC/OS-II (sending)
CAN_RESULT CANSendFrame(CAN_ID id, INT8U length, INT8U *data)
  Sends a message with id and data stored in the data array of length length.
  Returns: CAN_OK

## Slide 41: Example: CAN under μC/OS-II (sending)
#define id 0x000000A8
void Task1(void) {
INT8U data[N];
/* populate the data array */
CANSendFrame(id, N, data);
}
void main(void) {
...
  CANInit();
CANConfigureBaudrate(125000, 0);
CANStart();
  ...
}

## Slide 42: Example: CAN under μC/OS-II (sending)
#define id 0x000000A8
void Task1(void) {
INT8U data[N];
/* populate the data array */
CANSendFrame(id, N, data);
}
void main(void) {
...
  CANInit();
CANConfigureBaudrate(125000, 0);
CANStart();
  ...
}
Notes: First we have to initialize internal data structures of the CAN driver, and setup the baud rate.

## Slide 43: Example: CAN under μC/OS-II (sending)
#define id 0x000000A8
void Task1(void) {
INT8U data[N];
/* populate the data array */
CANSendFrame(id, N, data);
}
void main(void) {
...
  CANInit();
CANConfigureBaudrate(125000, 0);
CANStart();
  ...
}
Notes: After everything is setup we must start the CAN driver, so that it starts listening on the CAN port for arriving messages and places them in the registered queue1s.

## Slide 44: Example: CAN under μC/OS-II (sending)
#define id 0x000000A8
void Task1(void) {
INT8U data[N];
/* populate the data array */
CANSendFrame(id, N, data);
}
void main(void) {
...
  CANInit();
CANConfigureBaudrate(125000, 0);
CANStart();
  ...
}

## Slide 45: Example: CAN under μC/OS-II (sending)
#define id 0x000000A8
void Task1(void) {
INT8U data[N];
/* populate the data array */
CANSendFrame(id, N, data);
}
void main(void) {
...
  CANInit();
CANConfigureBaudrate(125000, 0);
CANStart();
  ...
}
Notes: Assemble the data which is to be sent (e.g. by reading a sensor) …

## Slide 46: Example: CAN under μC/OS-II (sending)
#define id 0x000000A8
void Task1(void) {
INT8U data[N];
/* populate the data array */
CANSendFrame(id, N, data);
}
void main(void) {
...
  CANInit();
CANConfigureBaudrate(125000, 0);
CANStart();
  ...
}
Notes: … and then send it.

## Slide 47: CAN under μC/OS-II (receiving)
  void* OSQPend(OS_EVENT *queue, INT16U timeout, INT8U *err)
    Reads a message from a queue. If queue is empty, the calling task will be suspended. Note that OSQ is part of the standard μC/OS-II API.
    Returns: a pointer to the message residing in the internal message buffer.
  CAN_RESULT CANForget(CAN_MSG* msg)
    Tells the CAN driver that the message was handled and that it can be removed from the internal message buffer.
    Returns:
      CAN_OK
      CAN_STILL_IN_USE if the message id was registered with several queues.

## Slide 48: CAN under μC/OS-II (initialization)
CAN_RESULT CANRegister(INT8U nids, INT32U* ids, OS_EVENT* queue)
  Registers a queue to receive pointers to those received messages which have an id equal to any integer in the ids array.
    The nids parameter should specify the length of the ids array. If nids is 0, then all messages that are received will be posted into the queue
    Registering the same queue more than once will cause duplicate pointers to be posted to the queue.
    Typically you will create and register one queue per task.
  Returns: CAN_OK
Notes: ThisCAN driver is very general, allowing each queueto wait for a subset of message ids, or several queues to wait for the same message id. This is why the nids and idlist parameters.

## Slide 49: Example: CAN under μC/OS-II (receiving)
#define id 0x000000A8
OS_EVENT* queue1;
void* queue1buf[10];
INT32U idlist1[1] = { id };
void Task2(void* pArg) {
INT8U err;
CAN_MSG* msg;
while (true) {
msg = (CAN_MSG*)(OSQPend(queue1, 0, &err));
if (err == OS_ERR_NONE) {
/* do something with msg */
}
CANForget(msg);
}
}
void main(void) {
...
  CANInit();
CANConfigureBaudrate(125000, 0);
queue1 = OSQCreate(queue1buf, 10);
  CANRegister(1, idlist1, queue1);
  CANStart();
  ...
}

## Slide 50: Example: CAN under μC/OS-II (receiving)
#define id 0x000000A8
OS_EVENT* queue1;
void* queue1buf[10];
INT32U idlist1[1] = { id };
void Task2(void* pArg) {
INT8U err;
CAN_MSG* msg;
while (true) {
msg = (CAN_MSG*)(OSQPend(queue1, 0, &err));
if (err == OS_ERR_NONE) {
/* do something with msg */
}
CANForget(msg);
}
}
void main(void) {
...
  CANInit();
CANConfigureBaudrate(125000, 0);
queue1 = OSQCreate(queue1buf, 10);
  CANRegister(1, idlist1, queue1);
  CANStart();
  ...
}
Notes: After the CAN driver is initialized we bind message ids to uC/OS-II queue1s, by registering a queue1 for an array of message ids.
Here the queue1buf is meant for actual storage of the pointers.

## Slide 51: Example: CAN under μC/OS-II (receiving)
#define id 0x000000A8
OS_EVENT* queue1;
void* queue1buf[10];
INT32U idlist1[1] = { id };
void Task2(void* pArg) {
INT8U err;
CAN_MSG* msg;
while (true) {
msg = (CAN_MSG*)(OSQPend(queue1, 0, &err));
if (err == OS_ERR_NONE) {
/* do something with msg */
}
CANForget(msg);
}
}
void main(void) {
...
  CANInit();
CANConfigureBaudrate(125000, 0);
queue1 = OSQCreate(queue1buf, 10);
  CANRegister(1, idlist1, queue1);
  CANStart();
  ...
}
Notes: The task has the standard uC/OS-II task structure: a while-true loop. Note that Task2 is NOT periodic, but its jobs are triggered by an arriving message.

## Slide 52: Example: CAN under μC/OS-II (receiving)
#define id 0x000000A8
OS_EVENT* queue1;
void* queue1buf[10];
INT32U idlist1[1] = { id };
void Task2(void* pArg) {
INT8U err;
CAN_MSG* msg;
while (true) {
msg = (CAN_MSG*)(OSQPend(queue1, 0, &err));
if (err == OS_ERR_NONE) {
/* do something with msg */
}
CANForget(msg);
}
}
void main(void) {
...
  CANInit();
CANConfigureBaudrate(125000, 0);
queue1 = OSQCreate(queue1buf, 10);
  CANRegister(1, idlist1, queue1);
  CANStart();
  ...
}
Notes: Each “job” of Task1 handles the arrival of a message via a queue1 previously registered with the CAN driver.
Note that Task1 will suspend on OSQPend() until there is a message to handle.

## Slide 53: Example: CAN under μC/OS-II (receiving)
#define id 0x000000A8
OS_EVENT* queue1;
void* queue1buf[10];
INT32U idlist1[1] = { id };
void Task2(void* pArg) {
INT8U err;
CAN_MSG* msg;
while (true) {
msg = (CAN_MSG*)(OSQPend(queue1, 0, &err));
if (err == OS_ERR_NONE) {
/* do something with msg */
}
CANForget(msg);
}
}
void main(void) {
...
  CANInit();
CANConfigureBaudrate(125000, 0);
queue1 = OSQCreate(queue1buf, 10);
  CANRegister(1, idlist1, queue1);
  CANStart();
  ...
}
Notes: If the message was properly received, then we can handle it (e.g. read the data in the message and perform a specific action)

## Slide 54: Example: CAN under μC/OS-II (receiving)
#define id 0x000000A8
OS_EVENT* queue1;
void* queue1buf[10];
INT32U idlist1[1] = { id };
void Task2(void* pArg) {
INT8U err;
CAN_MSG* msg;
while (true) {
msg = (CAN_MSG*)(OSQPend(queue1, 0, &err));
if (err == OS_ERR_NONE) {
/* do something with msg */
}
CANForget(msg);
}
}
void main(void) {
...
  CANInit();
CANConfigureBaudrate(125000, 0);
queue1 = OSQCreate(queue1buf, 10);
  CANRegister(1, idlist1, queue1);
  CANStart();
  ...
}
Notes: After we are done with the message, we have to tell the CAN driver to dispose of it in its internal data structures.

## Slide 55: References
Recommended reading:
  [Burns]: Ch. 11.14
Further reading:
  [Burns]: Ch. 11.10.3
  R.I. Davis, A. Burns, R.J. Bril, and J.J. Lukkien, Controller Area Network (CAN) schedulability analysis: Refuted, revisited and revised, Real-Time Systems, 35(3): 239-272, April 2007